Polluted Places - Sampling Results:

Haina Battery Recycling Plant (legacy site)

Haina, Dominican Republic

Address:	Paraiso de Dios, Haina (North 18º 25.849, West 70º 01.129)

Date:	20 Feb. 2006

Name:  	Jack Caravanos and Richard Fuller

Samples Taken:

A preliminary site sampling was conducted on February 20th 2006. Lead levels were tested in a stratified sampling scheme for soil and a single interior floor dust was collected and analyzed. All samples were sent to an US EPA accredited lead analytical laboratory. (i.e. Schneider Laboratories - Richmond VA) and analyzed according to EPA method 7420.

Soil Samples (3 areas were sampled for a total of 28 samples):

- Battery recycling facility (property) – the site was divided into 12 equally sized areas and one soil sample was collected from the center of each quadrant. Each sample consisted of a 5 part composite to ensure adequate representation. Meaning, 5 samples were taken from each quadrant (an area approximately 1 square meter) and combined.  See Table 1 for results

- Perimeter Sampling: 12 soil samples were taken from the perimeter of the facility on all 3 sides. Often this was done within a residential backyard. Summary statistic are presented in Table 2

TABLE 1: Perimeter and Legacy Site Lead in Soil Levels

|  | Lead in Soil Levels (ppm or mg/kg) |
| --- | --- |
| Sample ID# (L or P) | Perimeter of Site | Legacy Site |
| 1 | 4,320 | 81,430 |
| 2 | 21,880 | 143,870 |
| 3 | 6,790 | 29,410 |
| 4 | 15,660 | 397,660 |
| 5 | 18,700 | 11,400 |
| 6 | 160 | 21,340 |
| 7 | 2,050 | 14,580 |
| 8 | 32,790 | 344,190 |
| 9 | 60,560 | 463,970 |
| 10 | 4,710 | 265,900 |
| 11 | 650 | 11,470 |
| 12 | 43,500 | 27,500 |

NOTE: 	USEPA Lead in Soil Health based standard is 400 ppm (or mg/kg). Bare soil/ child contact.

Sample ID#’s for perimeter and legacy site do not match in location

(see attached diagram for sample location)

TABLE 2: Summary Statistics for Perimeter and Legacy Site Lead in Soil Levels

|  | Perimeter of Site | Legacy Site |
| --- | --- | --- |
| Median | 11,225 | 55,420 |
| Minimum | 160 | 11,400 |
| Maximum | 60,560 | 463,970 |
| 90th percentile | 42,429 | 392,313 |

- Runoff (outflow) Sampling: 4 soil samples were taken “downstream” from the lowest portion of property where rain runoff flows to the Haina River. These samples were also 5 part composites taken equidistant from the property and in the middle of road). (see Table 2 for results)

TABLE 3: Outflow Lead in Soil Levels

|  | Distance from “ravine” | ppm-Pb (or mg/kg) |
| --- | --- | --- |
| Outflow 1 | 20 yd | 7,270 |
| Outflow 2 | 100 yd | 80 |
| Outflow 3 | 200 yd | 290 |
| Outflow 4 | 300 yd | 70 |

Dust Samples:

- A single floor dust wipe sample was taken from inside the food store (bodega) for the analysis of lead. The sampling site measured 17” x 9” and was taken from the middle of the floor in front of the counter.

  - Result - 496.5 micrograms per square foot

  - The US EPA Lead floor dust hazard standard is 40 mcg/sf.

Drawing not to scale

# Text boxes

P7

P6

P5

P4

P3

Battery Recycling Facility (Legacy Site)

P2

P1

P81

P9

P10

Calle Cabon (paved road)

P11

P12

Ravine (excavated)

L1

L2

L3

L4

L5

L6

L7

L8

L9

L10

L12

L11